## Slide 1: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg

## Slide 2: Discussion regarding Assignment 3
Assignment 3: April 8th April
Submission after deadline: Penalty of 10% Per Day (Last date: 15th April)
Additional sensor tags are available if required
  Please email: Dhairya Shah (details on course page)
Please submit statement of work and report. The statement of work should describe the contribution made by every member of the group. Only one member should submit the assignment on the canvas.

## Slide 3: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Localization continued
Node discovery
Wide area networks
Routing
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 4: Medium access control for Internet of Things
Medium access control for normal wireless devices
  Low Latency
  High Utilization
  Fair (every has chance to communicate)
How about medium access control for internet of things?
  Power Consumption should be as small as possible
  (Most) sensor applications have low channel utilization
Designing medium access control with energy consideration as priority?

## Slide 5: Energy consumption of medium access control
The main sources of energy consumption in any contention-based MAC protocol:
  overhearing
  control packet overhead
  data transmission/reception
  idle listening
(1) – (3) occurs only when there is a transmission
(4) occurs even when there is no traffic

## Slide 6: “Life Cycle” of MAC Protocols
(4)
(1) – (3)
(4)
(1) – (3)
(4)
(1) – (3)
Less Traffic
(4)
(1 – (3)
(4)
(1) – (3)
Less Traffic
(4)
(4)

## Slide 7: Aloha with Preamble Sampling
Preamble
Data
Sender
Receiver
Sensing
Sensing
Sensing
Sensing
Receiver 1
Sensing
Sensing
ACK
Recv
Receiver 2
Sensing
Sensing
(Possible we can miss the preamble and thus data?)
Sensing

## Slide 8: Aloha with Preamble Sampling
Each receiver periodically (every Tp) wakes up to check if the channel is busy for a duration of (Ts)
  If channel is busy, stays in listening mode until destination of data is known (transmitted), else go back to sleep for a period of (Tp-Ts)
Sender transmits a long preamble (Tp), and then send data packet at the end of the preamble period of packet transmission
Is this protocol energy efficient? Why? And Why Not?
Preamble
Data
Sender
Receiver 1
Sensing
Sensing
ACK
Recv
Sensing
Tp
Ts
TD

## Slide 9: B-MAC: Asynchronous Medium Access Control
B-MAC asynchronous MAC protocol. Based on concept of preamble sampling
Nodes periodically activate their radios to detect signals; remain active upon receiving a packet or go to sleep after a set timeout if no activity is detected
To guarantee packet reception, the preamble duration must be at least as long as the channel sampling rate
The preamble time (Tp) should align with the channel check interval for reception; for instance, a 100ms check requires a minimum 100ms preamble

## Slide 10: Improving B-MAC with X-MAC
X-MAC improves over B-MAC
  Sender transmits many “probes” with gaps between probes. Each probe contains address of intended receiver
  Receiver checks address embedded in probe, sends acks if it is the destination during the gap period between probes
  Sender transmits DATA, receive replies with Ack to complete data transfer

## Slide 11: ContikiMAC
ContikiMAC is the MAC protocol implemented in Contiki OS

## Slide 12: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Localization continued
Node discovery
Wide area networks
Routing
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 13: What do you mean by the term localization?
Localization systems determine the physical coordinates of an electronic device such as IoT nodes, drones, mobile phones or a subject
These physical coordinates of electronic devices are:
  Global - aligned with some externally meaningful systems like GPS
  Relative - some “rigid transformation” (rotation, reflection, translation) away from a global coordinate systems
Localization indoors: goal is positioning things within a building
  Where can I find X?
  X: where am I located?
  X and Y: are we near each other?

## Slide 14: Overview of Global Positioning System
Satellites placed in Medium Earth Orbit (20,000 KM)
  Orbit earth twice per day
  Placed such that 4 are in view everywhere, always
  31 total in orbit as of November 2020
    Most recent launch November 5th 2020
Comparisons
  LEO 200-2000 km, ISS at 340 km
  GEO 35,000 km

## Slide 15: Global Positioning Service
How does GPS work?
  Know the position of all satellites
  Receive signals from multiple satellites
  Determine distance from each satellite
  Trilateration

## Slide 16: GPS PHY
GPS frequency
  1.2 GHz and 1.5 GHz
  10-15 MHz bandwidth
BPSK modulation
Signal has to travel 20,000 km, but most of that is through space
  Tx power 25 Watts (44 dBm)
  Rx sensitivity -140 dBm to -160 dBm (50 bps data rate)
  ~200 dBm total link budget

## Slide 17: GPS transmissions
Each satellite sends a unique pseudo-random number sequence
  Sequence repeats in time (over minutes) and is well-known
  Position in signal is used to calculate time of flight

## Slide 18: GPS requires signals from multiple satellites
4 satellites are needed to determine location and time
  3 for 2D location (assume on ground) and 1 for time offset
  Solve for both as a single equation
Steps to finding location
  Initialize time to whatever you heard from a satellite (~100 ms sync)
  Get time of arrival from four satellites
  Four variables
    x, y, z, and time offset

## Slide 19: What is trilateration?
Determine distance from each beacon, then find position
  Apply trigonometry to solve triangle with beacons.
  Requires: 3 lengths (or some angles and lengths…)
  Solve two triangles and get 3D position
Most common and accurate localization approach

## Slide 20: How to determine distances?
Making trilateration work requires distance measurements
There are numerous techniques for distance measurement
  RSSI (Received Signal Strength Indicator)
  Time of Flight/ Time of Arrival
  Time Distance of Arrival

## Slide 21: Received Signal Strength Indicators (RSSI)
RSSI - received signal-strength indication
In theory, RSSI varies with 1/d
  One common assumption, nodes that are closer have stronger RSSI than those further
In practice, RSSI ranging measurements contain noise on the order of several meters, highly non-uniform
  Radio propagation differs over different surface (water, grass, asphalt etc.)
  Obstacles such as wall, furniture etc.

## Slide 22: Problem with RSSI-based distance – not accurate
Pathloss is NOT only due to distance
RSSI is way worse at this than you hope it would be
Citation: literally everyone has made this figure at some point

## Slide 23: Time of flight (also known as time of arrival, ToA)
Determine distance by knowing:
  Exact position of infrastructure
  Transmit time
  Receive time
  Signal velocity (i.e. speed of light)
Infrastructure transmits and device listens
  Can happen all the time, but devices only listen when they want a position
Requires time synchronization between infrastructure and device
  Synchronization must be good: 1 μs = 300 meters

## Slide 24
Important Considerations:
Speed of signal propagation
Distance to be measured
Clock accuracy
Example:
Speed of light (c) ~ 3x108 m/s
Distance travel in 1ms = 300m
Clock accuracy needed for meter accuracy (1/c) ~ 3ns
Speed of sound (v) ~ 330 m/s
Distance travel in 1ms = 0.33m
Clock accuracy needed for meter accuracy = 1/v ~ 3ms
Time of flight (also known as time of arrival, ToA)

## Slide 25: Ultrasound
Advantages
  Solves the barrier problem
    Human spaces already designed to contain sound
  Easier to get high-accuracy results
    Sound is ~1,000,000x slower than light
    Less synchronization is needed to get same accuracy
Disadvantages
  More energy to transmit
  Slower update rate (still sub-second)
  Limited range
  Pets can hear it…

## Slide 26: Time difference of arrival (TDoA)
Device transmits and infrastructure receives transmission
  Multiple infrastructure nodes receive at different times based on distance
Determine distance by knowing
  Exact position of infrastructure
  Time of arrival at two different locations
  Signal velocity (i.e. speed of light)
Doesn’t require synchronization with infrastructure!
  Still requires synchronization between infrastructure nodes
  Does require device to transmit loud enough for infrastructure to hear it…

## Slide 27: Time difference of arrival with different mediums
Exploit differences in speed, say RF and audio
Example: Cricket System [1]
  In addition to a radio, each node also has a speaker and microphone
How does Cricket works?
Transmitter sends a radio message, waits some time (optionally) t_delay, sends audio “chirp” sound
Listener hears the radio signal, record time t_radio
Listener hears the audio signal, record time t_sound
[1] http://cricket.csail.mit.edu/

## Slide 28
Time diff between signal arrival = d/SSound – d/SRadio + tdelay
Works well in LOS environment
  Cricket (uses ultra sound) can obtain close to cm accuracy
Requires additional hardware and works better with calibration
Time difference of arrival with different mediums

## Slide 29: Angle of arrival (AoA)
Trilateration doesn’t only require distances, angles work
Antenna arrays can be used to determine the angle of an incoming signal
  Allows the use of normal RF communication (WiFi or BLE)
BLE 5.1 includes AoA localization

## Slide 30: Mapping existing infrastructure
Can we repurpose existing infrastructure for localization?
  For example: WiFi access points
  Benefit: localization works with unmodified hardware
Mapping instead of trilateration
  Make a map of infrastructure and use that to locate device
  Coarse example: existence of WiFi network SSIDs
  Fine-grained example: signal strength to each Access Point
    Known as fingerprinting

## Slide 31: Fingerprinting overview
At setup time, for many locations throughout building
  Measure signal strength to Access Point
  Record measurement in a database with location
At run time, for the device that wants a location
  Measure signal strength to Access Point
  Look up measurement in database to get location

## Slide 32: Fingerprinting improvements
Measurements can use several Access Points simultaneously
  Improves accuracy quite a bit
Doesn’t have to be WiFi based at all
  Cellular networks can do fingerprinting
  Deploy your own BLE beacons throughout environment
Apply techniques for minimizing error in signal strength
  Measurement won’t match record exactly
  But minimizing error should approach the same location

## Slide 33: Fingerprinting challenges
Effort to create database in the first place
  Manually take measurements at every location
Environment is not stable
  Signal strength changes as chairs, doors, and people move
  Need ability to periodically re-measure
    Update database with most recent recording while in use
Measurements vary between devices
  Differ based on antennas, cases, how you hold it, etc.

## Slide 34: Fingerprinting accuracy
State-of-the-art: median accuracy of 0.5-1.5 meters
  Not bad depending on the application!
  Likely places you in the right room, or at least nearby
  Long tail can be large, but more access points helps this
Barrier problem capability depends on walls
  Some materials attenuate signal strength more than others

## Slide 35
Similarity of WiFi Fingerprints
Hong, Hande, et.al. "Socialprobe: Understanding social interaction through passive wifi monitoring." Mobiquitous 2016.

## Slide 36: Localization using (WiFi) Fingerprinting
RADAR is one of the earliest & most highly cited localization using WiFi based fingerprinting (>12,000 citations on scholar.google.com)
Testbed:
  1 floor, 980 sq. meters, 50 rooms
  3 base stations, 1 mobile host

## Slide 37: Inertial navigation
If you know acceleration, you can get position, just integrate!
  With quite a bit of error
Accurate over short distances with filtering approaches
  Can be used to augment other systems
  Get a fix every few seconds from localization system
  Use inertial navigation to interpolate between measurements
IMUs (Inertial Measurement Units) available in all smartphones
  Accelerometer, Gyroscope, Magnetometer

## Slide 38: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Localization continued
Node discovery
Wide area networks
Routing
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 39
Node Discovery

## Slide 40: How to discover nodes or devices nearby
Scenarios for local discovery
  You just enter a shopping mall. You would like to check if there is WiFi service. How does your mobile phone discover the presence of WiFi networks?
  Small devices with low power network interface (e.g. ZigBee) are deployed in the surrounding and carried by humans. How can these devices discover other devices in range (in an energy efficient way)?

## Slide 41: How to perform neighbor discovery?
Problem is “easy” to solve if there is no constraint and all nodes can be active all the time.
  Challenge is to design a protocol that is energy efficient.
Two broad methods for local neighbor discovery:
  Synchronous
  Asynchronous

## Slide 42: Synchronous neighbor discovery
All nodes are synchronized to the same clock/time.
Nodes wakeup periodically at same time to transmit/receive packets
Node A discovers node B when it hears a transmission from node B
Example:
  Time divided into slots of 100ms and there is a global starting reference time t0 sec
  With a 10% duty cycle, period is 1s,
    each node wakes up at t0 + k sec for 100ms, where k = 0,1,2,3,4….
  With a 1% duty cycle, period is 10s,
    each node wakes up every t0 + 10k sec for 100ms, where k = 0,1,2,3,4….

## Slide 43: Drawbacks to synchronous neighbor discovery?
Synchronization can be expensive and periodically re-synchronization will be needed to correct for clock drift over time
As all nodes wakeup at the same time to transmit/receive, collision may increase if too many node transmit simultaneously

## Slide 44: Synchronous neighbor discovery with Asymmetric Nodes
Some nodes are more powerful and is always “ON”
Example: WiFi APs (always ON) vs. mobile device (stays in OFF state as much possible)
A mobile device wants to discover nearby APs
  APs are always awake
  Mobile device broadcasts (how often?) a probe beacon and listens for replies
    How about AP periodically broadcasts and mobile replies?
A mobile device is associated with an AP but wants to conserve energy by going into sleep state whenever there is no data communication
  How does the device know there is data from the AP if it is in sleep state?

## Slide 45: Power Save Mode (Infrastructure)
When a mobile device wants to go into Power Save Mode (PSM), it informs the AP and goes into sleep state (switches off its radio)
Any packets arriving at the AP for the mobile device in PSM are stored in the AP’s buffer
The AP sends a beacon frame after every fixed time interval. The beacon frame has a field called traffic indication map (TIM) to inform the device in PSM about incoming packets.
Device in PSM wakes up periodically to listen to beacon frames and switch to active state if there are incoming packets

## Slide 46: Asynchronous Protocols
Challenges:
  No time synchronization
  All nodes are resource constrained
Assumptions
  Divide into time slots (e.g. 100ms)
  Each device decides (randomly?) which time slots to wakeup to transmit/listen
How long will two such devices take to discover each other?

## Slide 47: Birthday Paradox
In a group of N people, what is the probability that there is at least one pair of people who have the same birthday? (assume 365 days in a year)
In general, Prob = 1 – P(none of the N people have the same birthday)
  N = 2, Prob = 1 – (364/365)
  N = 3, Prob = 1 – (364/365)(363/365)
  N = 4, Prob = 1 – ((364/365)(363/365)(362/365)
  N = n, Prob = 1 – 365!/(365n(365-n)!)
Example:
  N = 2, Prob = 0.0027
  N = 23, Prob = 0.5073
  N = 50, Prob = 0.9704

## Slide 48
“Birthday” Protocol
Easy to implement
Good average discovery latency but unbounded worst case

## Slide 49: Application to Asynchronous Discovery Michael J McGlynn and Steven A Borbash. Birthday protocols for low energy deployment and flexible neighbor discovery in ad hoc wireless networks. In MobiHoc, 2001
Two nodes randomly choose to wakeup k time slots out of a total n slots. What is the probability that they wakeup at the same time slot at least once?
Probability (Q) can be written down as:
(1%) n = 100, k = 1, Q(100,1) = 0.01
(5%) n = 100, k = 5, Q(100,5) = 0.23
(1%) n = 1000, k = 10, Q(1000,10) = 0.096
(5%) n = 1000, k = 50, Q(1000, 50) = 0.928
Drawbacks – probabilistic bound for discovery time, can take very long sometimes
Can we do better in terms of the worst case?

## Slide 50: DISCO - Asynchronous neighbor discovery algorithm
Scheduling radio wake times at multiples of prime numbers to ensure deterministic discovery
  Nodes can have different duty cycles
Version 0: A node i picks a prime number, say pi and wakes up pi timeslots, the duty cycle is (1/ pi). In the worst case, two nodes pi and pj will meet after (pi * pj) timeslots.
  Problem: what if both nodes pick the same prime number?
Version 1: A nodes i picks a prime number, say pi1 and pi2 (pi1 != pi2), wakes up every pi1 and pi2 timeslots. The duty cycle is (1/pi1 + 1/pi2)
  If both nodes pick the same pair of prime number:
    Duty cycle ~ (pi1 + pi2)/ pi1 pi2, Worst Case ~ pi1 pi2
Dutta, Prabal, and David Culler. "Practical asynchronous neighbor discovery and rendezvous for mobile sensing applications." Proceedings of the 6th ACM conference on Embedded network sensor systems. 2008.

## Slide 51: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Localization continued
Node discovery
Wide Area Networks
Routing
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 52
Wide-Area Networks

## Slide 53: Air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2018.
[1]
[1]
[2]
[2]

## Slide 54: Audio detection, classification, and localization
[1] Girod et al. The Design and Implementation of a Self-Calibrating Distributed Acoustic Sensing Platform. 2006. [2] Lédeczi et al. Multiple Simultaneous Acoustic Source Localization in Urban Terrain. 2005. [3] Sounds of New York City. 2016.
[1]
[1]
[2]
[3]

## Slide 55: Traffic queue sensing and congestion control
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012
[1]
[1]
[1]

## Slide 56: Example application: air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2019.
[1]
[2]
[2]

## Slide 57: How do we collect data from a sensor?
Manually collect measurements
Connect it to WiFi (or Ethernet)
Pay for cellular access

## Slide 58: How do we collect data from MANY sensors?
Manually collect measurements
  Too much work
Connect it to WiFi (or Ethernet)
  Too many separate networks
Pay for cellular access
  Too expensive for many devices

## Slide 59: We need another network option
Requirements:
Wide area of coverage
  Deploy fewer gateways
Low power
  So we can deploy on batteries
Doesn’t need high throughput
  Sensor data is relatively small

## Slide 60: Long-range,low-data needs are not easily met
Data
Throughput
Range
WiFi

## Slide 61: Long-range,low-data needs are not easily met
Bluetooth
WiFi
BLE
Zigbee
Data
Throughput
Range

## Slide 62: Long-range,low-data needs are not easily met
Bluetooth
WiFi
BLE
Zigbee
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 63: Long-range,low-data needs are not easily met
Bluetooth
WiFi
2G
3G
4G
BLE
Zigbee
2G
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 64: Long-range,low-data needs are not easily met
Bluetooth
WiFi
3G
4G
BLE
Zigbee
Low-Power Wide-Area Networks
2G
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 65: Long-range, Low-power: design choices
How would you design PHY for long-range, low-power ?

## Slide 66: Long-range, Low-power: design choices
How would you design PHY for long-range, low-power ?
  Modulation
  Tx Power
  Carrier Frequency Band
  Data Throughput
  Channel Bandwidth

## Slide 67: Long-range, Low-power: design choices
How would you design PHY for long-range, low-power ?
  Modulation
    Unclear. Perhaps, not complicated or complex (simple devices)
  Tx Power
    High (much higher than 0 dBm)
  Carrier Frequency Band
    Low (something lower than 2.4 GHz, 915 MHz or lower?)
  Data Throughput
    Low (much lower than 1 Mbps)
  Channel Bandwidth
    Unclear. Likely smaller for lower frequency carrier.

## Slide 68: Long range backscatter transmissions using LoRea
LoRea is a long range, low-power, and low-cost backscatter architecture
Backscatter Tag Hardware Prototype
(Peak Power of 70 µW)
System Overview
Varshney et al. ”LoRea: A Backscatter architecture that achieves a long communication range” ACM SENSYS 2017
Notes: + Over the past several years, I have designed systems that overcome these critical limitations that have hindered the backscatter systems and have the prevented widespread adoption of the backscatter mechanisms on the Internet of Things devices. One of these systems is LoRea.
+ LoRea was presented at ACM SENSYS, which is a flagship conference in the area of embedded sensor systems. I show the architecture of LoRea on the left-hand figure on the slide. It consists of one or more commodity devices such as a smartphone or Wi-Fi router that provides the necessary carrier signal to support backscatter transmissions, a low-power backscatter tag that I had designed and transmit at a peak power of 70uw, and one or more receiver of backscatter transmissions.
+ The key highlight of LoRea was that it could achieve a significantly larger communication range than existing systems, was designed using off the shelf components and cost (few tens of USDs). Further, the backscatter tag could achieve this capability at orders of magnitude lower energy than commercially available radio transceivers.
+ How did LoRea achieve this capability? We would describe next.

## Slide 69: LoRea backscatter narrow bandwidth transmissions which improves sensitivity
Key idea: Receiver sensitivity improves as we lower bandwidth
Lower bitrate (2.9 kbit/s) generates narrow bandwidth transmissions
Low bitrates are not detrimental to most sensing applications
Operating frequency | Bandwidth
868 MHz | 13 kHz
2.4 GHz | 180 kHz
Notes: + The third design element that we incorporate in LoRea enables us to significantly improve the communication range. We use key idea that the receiver sensitivity improves as we lower the bandwidth and bitrate. In LoRea, we intentionally generate narrow bandwidth transmissions, in fact, in LoRea we transmit at 2.9 Kbits and generate transmissions of 13 KHz bandwidth. Just compare this to WiFi which takes tens of MHz of bandwidth for transmissions.
+ This design element allows us to use highly sensitive radio transceievers for reception of backscatter transmissions, in fact, we use CC1310 which supports a very high sensitivity of -124 dBm which enables us to support very high link budget and communication range.
+ You might wonder: Doesn’t this impact the application scenarios? No, it does not. This is because most sensing applications transmit only small bits of information periodically, and hence the lower bitrate is not detrimental to their operation.

## Slide 70: Long range depends on receiver sensitivity and transmit power
Receiver sensitivity improves with lower bitrate/bandwidth
Low bitrate, narrow band signals, very high receive sensitivity
Large transmit power, high receive sensitivity -> Very large range
LoRea: -124 dBm at < 1 kbps, 2 FSK

## Slide 71: Design a low-power wide-area network
Any particular MAC choices for lower power?
  Diversity of devices in network
    High power gateway, low power devices in star topology
  Devices should be off whenever possible
    Listen-after send for downlink
  Remove requirements for synchronization
    No TDMA access control if it can be avoided
    Aloha, CSMA

## Slide 72: Long-range CSMA is problematic
Long-range makes everything more challenging
  Kilometers of range mean kilometers between devices
Detection of channel use is less reliable
  Active research in clear channel assessment for LPWANs
Hidden terminal problem has a wider range
  Might make RTS/CTS more important
Result: CSMA doesn’t dominate LPWANs like it does WLANs

## Slide 73: LPWANs overview (common qualities)
Unlicensed 915 MHz band (902-928 MHz)
Higher power transmissions: ~20 dBm (100 mW)
Low data rate 100 kbps or less
Range on the order of multiple kilometers
Simple Aloha access control

## Slide 74: Overview of LoRa standard (Courtesy: Semtech)

## Slide 75: LoRaWAN
Open communication standard built with proprietary LoRa PHY
Operates in the unlicensed band
Low data rate (1-20 kbps) and long range (~5 km)
Most popular LPWAN protocol
  Academic research and industry involvement

## Slide 76: LoRa employs a different modulation scheme
Chirp Spread Spectrum (CSS): Modulation technique where frequency is varied linearly from lowest to highest within a channel

## Slide 77: Chirp Spread Spectrum
Data is modulated in the starting and ending points of chirp
  Frequency increases linearly, modulo bounds of the channel

## Slide 78: Spreading factor of CSS modulation
Spreading Factor is essentially the rate-of-change of frequency
  Slope of the line
  Lower values of spreading factor (steeper slope) are faster data rate
Important: different spreading factors are (mostly) orthogonal!
  Two can overlap in time, space, and channel without a collision

## Slide 79: Overview of CSS (brief video)

## Slide 80: Channel allocation for LoRa
Sixty-four, 125 kHz uplink channels
  Frequency Hopping over the 64 uplink channels
  Plus eight, 500 kHz overlapping uplink channels (not well used in practice)
Eight, 500 kHz downlink channels

## Slide 81: LoRa data rates
Data Rate Index | Spreading Factor | Bit Rate
125 kHz Uplink Rates |  | 
0 | SF10, 125 kHz | 980 bps
1 | SF9, 125 kHz | 1760 bps
2 | SF8, 125 kHz | 3125 bps
3 | SF7, 125 kHz | 5470 bps
500 kHz Uplink Rates |  | 
4 | SF8, 500 kHz | 12500 bps
500 kHz Downlink Rates |  | 
8 | SF12, 500 kHz | 980 bps
9 | SF11, 500 kHz | 1760 bps
10 | SF10, 500 kHz | 3900 bps
11 | SF9, 500 kHz | 7000 bps
12 | SF8, 500 kHz | 12500 bps
13 | SF7, 500 kHz | 21900 bps
Data rate depend on channel in use, spreading factor
64-channel uplink
  1-5 kbps data rate

## Slide 82: LoRaWAN MAC
Uplink: Aloha - transmit whenever
  Randomly split across 64 uplink channels (reduced odds of collision)
  Devices a different spreading factors also do not collide
  Packets are very long though: up to 400 ms in duration
Downlink: listen-after-send (class A device)
  Two windows for RX on different channels

## Slide 83: LoRaWAN packet format
Frame header includes device address
MAC Payload maximum size depends on data rate
  Again based on dwell time in the US
Data Rate Index | MAC Payload Size
0 | 19 bytes
1 | 61 bytes
2 | 133 bytes
3 | 250 bytes
4 | 250 bytes

## Slide 84: LoRa link budget and transmission range
Typical TX power 20 dBm
  Up to 30 dBm for 64-channel hopping
  Up to 26 dBm for 8-channel hopping
Receive sensitivity -119 dBm/-146 dBm (highest SF)
  Compare to -100 dBm for 802.15.4 and -95 dBm for BLE
Resulting range is kilometers in urban environments

## Slide 85: You can build your own LoRa network
Easy-to-use, off-the-shelf hardware available (tens of USD)
Could be useful for projects that you may do in this course

## Slide 86: LoRaWAN network providers
Network provides with a deployment of gateways
  The Things Network (predominantly in Europe)
  Helium
    Any can buy and install their own gateway, which serves everyone
    Microtransactions to pay for communication

## Slide 87: TTN Scale [Jan 2022]

## Slide 88: Helium Scale [Jan 2022]

## Slide 89: Sigfox
Very low-rate (600 bps), very long-range (10+ km) communication
Star-topology networks, with always-listening gateways
  Any number of low-power end devices
Uplink-focused communication
Applications: very low-rate metering

## Slide 90: Sigfox PHY
Unlicensed-band communication
  Europe 868 MHz. US 902-928 MHz (915 MHz band)
Ultra-narrowband 600 Hz (100 Hz Europe) channel bandwidth
  Detection only needs to occur at very specific frequency
  Helps improve signal-to-noise ratio

## Slide 91: Sigfox unbalanced uplink and downlink
Uplink
  600 Hz bandwidth, 600 bps, DBPSK
Downlink
  1.5 kHz bandwidth, 600 bps, GFSK
Particularly optimized for Europe
  Uplink on 1% duty cycle channel, up to 14 dBm
  Downlink on 10% duty cycle channel, up to 27 dBm
Works fine in US too
  Gets more power (24 dBm up is typical, up to 32 dBm down) and more range

## Slide 92: Sigfox link budget
Why transmit at 100-600 bps?
  For greatly increased link budget
Link budget: 150-160 dBm
  Assuming Tx at ~20 dBm
  Means Rx Sensitivity of -130 dBm (10 dBm better than LoRaWAN)
Resulting range: 10-15 km in urban environments
  Except that buildings lead to dead spots in range

## Slide 93: Sigfox MAC
Aloha-style access control (send whenever)
  No acknowledgements!
Send message three times for increased reliability
  Then listen for downlink at a set period later on a known frequency

## Slide 94: Sigfox uplink packet
Up to 29 bytes total per packet
  Payload: up to 12 bytes
Other fields
  Preamble + Frame Sync are really a 6 byte field for radio sync
  Authentication: 2-5 bytes
  Frame Check Sequence: 16-bit CRC

## Slide 95: Sigfox downlink packet
Similar structure, 28 bytes total
  Payload: up to 8 bytes
Larger preamble + frame sync of 13 bytes
Error Correcting Code for increased reliability

## Slide 96: Sigfox deployments
Proprietary network with managed deployment
  Like cellular networks
  Sigfox deploys networks and transports data
  140 uplink messages plus 4 downlink message per day
Connectionless communication
  Devices are registered with the networks
  Keys are provided in the software image
  Any deployed Sigfox gateway can collect transmitted data
    Enables mobile applications

## Slide 97: IEEE standard for LPWANs
802.11ah (HaLow) standard in 2016
  First real hardware in 2020
  Still not in real-world use yet
Focus on the indoor-to-outdoor scenario
  Medium range (maximum 1 km)
915 MHz communication
  NOT interoperable with other 802.11 access points and devices
Theoretically up to 356 Mbps
  Practically, most devices are expected to implement 150 kbps to 8 Mbps
n.b.
802 = “area networking”
.3 = “LANs”
.11 = “Wireless LANs”
.15 = “PANs”

## Slide 98: 802.11ah allows multiple bandwidth allocations

## Slide 99: WiFi Hallow Range Test (Courtesy: Newracom)

## Slide 100: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Localization continued
Node discovery
Wide Area Networks
Routing
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 101
Routing

## Slide 102: What do you mean by routing?
Have a packet, have a destination, how do we network them?
Routing is trivial if all nodes are connected to each other
Problem: if N nodes, need N(N-1) or O(N2) (uni-directional) links
Trivial for wireless, but number of links may grow.
  Simple techniques: broadcast, tree structures
  Mesh techniques: understand available routes and select a “good” one

## Slide 103: Performing routing in the wired networks
Number of links can be reduced significantly with one “BIG” switch with N links and routing is still simple
Problem: If N is large and nodes can be far apart (think of the Internet)
Adding more switches/routers reduces the size of the switches/routers needed and allow network to grow
But Routing will be more complex!

## Slide 104: Performing routing in the wireless networks
Routing protocols are complex, hard to maintain/debug and incurred significant overhead. More so for wireless networks.
In practice, wireless network deployments are single-hop and routing is trivial. All stations/devices communicating directly with base stations
  Example: WiFi, Cellular Network, LoRa
  Can one-hop communication be always sufficient by using sufficiently long range radio and large number of base stations?
Why multi-hop routing?
  is strictly better in terms of reach/coverage for the same number of base stations
  provides more routes, potentially more robust

## Slide 105: For the same distance, is it better to have direct or multi-hop path?
A
B
A
D
C
B
E
Which option is better?
Typically, a single-hop is considered better

## Slide 106: But, for energy Consumption …
Is multiple-hop transmission more energy efficient than a single-hop ?
Let us Recall the free space model: Pr = C Pt / da (C = constant)
Transmission over a distance d, let minimum received power needed be P0
  1 transmission to cover distance d, transmission power (P1) needed is
    P0 = C P1 / da or P1 = P0/C * da
  N transmissions to cover distance d, transmission power needed (PN) per hop is
    P0 = C PN / (d/N)a , or PN = P0 /C * (d/N)a
    Total transmission power is N PN = N P0 /C * (d/N)a
Which approach (1 transmission vs N transmissions) is more energy efficient?

## Slide 107: Classification of c routing protocols
The existing routing protocols can be classified as:
  Proactive: when a packet needs to be forwarded, the route is already known
  Reactive: Determine a route only when there is data to send

## Slide 108: Many-to-one routing
Tree optimization for sensor networks
  Keep all devices except the “gateway” as simple as possible
Each device only needs to remember hop to gateway
  If gateway wants to send message back, it must include a full hop path

## Slide 109: Mesh Routing
Formed by a network of static wireless nodes
Mesh topology makes routing question more complicated
  Multiple hops in a route
  Multiple routes between source and destination
  Becomes a graph theory question based on cost metric
A
B
C
D
E
F

## Slide 110: Flooding
Mesh equivalent of broadcast
  Each node sends to each other node
  Eventually packets will reach the desired destination
  Not really routing at all…
Question: how do we make it stop?

## Slide 111: Flooding
Mesh equivalent of broadcast
  Each node sends to each other node
  Eventually packets will reach the desired destination
  Not really routing at all…
Question: how do we make it stop?
  Maximum retransmissions counter on each packet
    Decrement at each hop. Drop packet when it hits zero
    Need some guess for how many hops to destination
  Keep some history of recently flooded packets
    Don’t retransmit a recently sent packet

## Slide 112: Roadmap of the lecture today
General course information and updates
Let us review what we had covered the last lecture
Localization continued
Node discovery
Wide Area Networks
Routing
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 113: Wireless Networking
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.